## Slide 2: กด swA ให้เลื่อนตำแหน่งไฟ swB ให้เปลี่ยสี
from machine import Pin
from neopixel import NeoPixel
from time import sleep
# Your NeoPixel initialization
np = NeoPixel(Pin(13, Pin.OUT), 25)
p = 0 # Initialize p to 0
sw1 = Pin(5, Pin.IN, Pin.PULL_UP)
sw2 = Pin(12, Pin.IN, Pin.PULL_UP)
colors = [(30, 0, 0), (0, 0, 30), (20, 0, 20), (0, 30, 0)] # Red, Blue, Purple, Green
color_index = 0 # Initial color index
while True:
# Check if sw1 is pressed to change the pattern
if sw1.value() == 0:
p = (p + 1) % 24
# Check if sw2 is pressed to change the color
if sw2.value() == 0:
# Cycle through the color list
color_index = (color_index + 1) % len(colors)
# Show the pattern with the selected color
for i in range(24):
if i == p:
np[i] = colors[color_index]
else:
np[i] = (0, 0, 0)
np.write()
sleep(0.2)

## Slide 3: กดปุ่ม A neopixel +1 iLED4 +1 กดปุ่ม B เปลี่ยนสี
import iLED4
from machine import Pin,ADC
from neopixel import NeoPixel
from time import sleep
adc = ADC(Pin(33)) # P2
adc.atten(ADC.ATTN_11DB)
# Your NeoPixel initialization
np = NeoPixel(Pin(13, Pin.OUT), 25)
p = 0 # Initialize p to 0
sw1 = Pin(4, Pin.IN, Pin.PULL_UP)
sw2 = Pin(2, Pin.IN, Pin.PULL_UP)
colors = [(30, 0, 0), (0, 0, 30), (20, 0, 20), (0, 30, 0)] # Red, Blue, Purple, Green
color_index = 0 # Initial color index
while True:
# Check if sw1 is pressed to change the pattern
if sw1.value() == 0:
p = (p + 1) % 24
iLED4.writeDigitNum(3,p%10,0)
iLED4.writeDigitNum(2,p%100/10,0)
# Check if sw2 is pressed to change the color
if sw2.value() == 0:
# Cycle through the color list
color_index = (color_index + 1) % len(colors)
# Show the pattern with the selected color
for i in range(24):
if i == p:
np[i] = colors[color_index]
else:
np[i] = (0, 0, 0)
np.write()
sleep(0.2)

## Slide 4: กดปุ่ม A neopixel +1 ZX-pot เปลี่ยนสี
from machine import Pin, ADC
from neopixel import NeoPixel
from time import sleep
adc = ADC(Pin(32))
adc.atten(ADC.ATTN_11DB)
sw1 = Pin(5, Pin.IN, Pin.PULL_UP)
# Your NeoPixel initialization
np = NeoPixel(Pin(13), 25)
p = 0 # Initialize p to 0
colors = [(30, 0, 0), (0, 0, 30), (20, 0, 20), (0, 30, 0)] # Red, Blue, Purple, Green
color_index = 0 # Initial color index
while True:
print(adc.read())
# Check if sw1 is pressed to change the pattern
if adc.read() <= 1000:
np[p] = colors[0] # Assigning Red color to the specific NeoPixel index
# Check if sw2 is pressed to change the color
elif adc.read() <= 2000 :
# Cycle through the color list
np[p] = colors[1]
elif adc.read() <= 3000 :
# Cycle through the color list
np[p] = colors[2]
elif adc.read() <= 4000 :
# Cycle through the color list
np[p] = colors[3]
if sw1.value() == 0:
p = (p + 1) % 24
# Show the pattern with the selected color
np.write()
sleep(0.2)

## Slide 5: neopixel rgb + ZX-POT
from machine import Pin, ADC
from neopixel import NeoPixel
from time import sleep
adc = ADC(Pin(32))
adc.atten(ADC.ATTN_11DB)
# Your NeoPixel initialization
np = NeoPixel(Pin(13), 25)
p = 0 # Initialize p to 0
colors = [(30, 0, 0), (0, 0, 30), (20, 0, 20), (0, 30, 0)] # Red, Blue, Purple, Green
color_index = 0 # Initial color index
while True:
print(adc.read())
# Check if sw1 is pressed to change the pattern
if adc.read() <= 1000:
np[p] = colors[0] # Assigning Red color to the specific NeoPixel index
# Check if sw2 is pressed to change the color
elif adc.read() <= 2000 :
# Cycle through the color list
np[p] = colors[1]
elif adc.read() <= 3000 :
# Cycle through the color list
np[p] = colors[2]
elif adc.read() <= 4000 :
# Cycle through the color list
np[p] = colors[3]
# Show the pattern with the selected color
np.write()
sleep(0.2)

## Slide 6: เมื่อให้ sonar มีค่า = 0 ให้ iled วิ่งจากขวาไปซ้าย
import iLED4
from machine import Pin, ADC
from time import sleep
adc = ADC(Pin(32, 33))
adc.atten(ADC.ATTN_11DB)
iii = 3
while True:
print('ADC=', adc.read(), 'RANGE', adc.read() / 40.95)
if adc.read() == 0:
for i in range (4):
iLED4.writeDigitRaw(i,0x01)
iLED4.writeDisplay()
sleep(1)
for ii in range (4):
iLED4.writeDigitRaw(ii,0x00)
iLED4.writeDisplay()
iLED4.writeDigitRaw(iii, 0x02)
iLED4.writeDisplay()
sleep(1)
iLED4.writeDigitRaw(iii, 0x04)
iLED4.writeDisplay()
sleep(1)
for i in range(3, -1, -1):
iLED4.writeDigitRaw(i, 0x08)
iLED4.writeDisplay()
sleep(1)
for ii in range(4, -1, -1):
iLED4.writeDigitRaw(ii, 0x00)
iLED4.writeDisplay()
iLED4.writeDigitRaw(0, 0x10)
iLED4.writeDisplay()
sleep(1)
iLED4.writeDigitRaw(0, 0x20)
iLED4.writeDisplay()
sleep(1)
else :
iLED4.writeDigitRaw(0, 0x20)
iLED4.writeDisplay()
sleep(1)
iLED4.writeDigitRaw(0, 0x10)
iLED4.writeDisplay()
sleep(1)
for i in range (4):
iLED4.writeDigitRaw(i, 0x08)
iLED4.writeDisplay()
sleep(1)
for ii in range (4):
iLED4.writeDigitRaw(ii, 0x00)
iLED4.writeDisplay()
iLED4.writeDigitRaw(iii, 0x04)
iLED4.writeDisplay()
sleep(1)
iLED4.writeDigitRaw(iii, 0x02)
iLED4.writeDisplay()
sleep(1)
for i in range(3, -1, -1):
iLED4.writeDigitRaw(i,0x01)
iLED4.writeDisplay()
sleep(1)
for ii in range(4, -1, -1):
iLED4.writeDigitRaw(ii,0x00)
iLED4.writeDisplay()

## Slide 7: เมื่อให้ sonar มีค่า = 0 ให้แสดงค่า iled 4 +1
from machine import Pin,ADC
import iLED4
from time import sleep
import display
adc = ADC(Pin(32))
adc.atten(ADC.ATTN_11DB)
led=Pin(2,Pin.OUT)
x = 0
while True :
print('ADC=',adc.read(),'RANGE',adc.read()/40.95)
sleep(0.1)
if adc.read() == 0 :
led(1)
x += 1
iLED4.writeDigitNum(3,x%10,0)
iLED4.writeDigitNum(2,x%100//10,0)
iLED4.writeDigitNum(1,x%1000//100,0)
iLED4.writeDigitNum(0,x%10000//1000,0)
else :
led(0)

## Slide 8: ควบคุม zx pot ให้แสดงบนiled4แล้วให้ servoหมุนตาม
import iLED4
from machine import Pin,ADC,PWM
from time import sleep
adc = ADC(Pin(32)) # P2
adc.atten(ADC.ATTN_11DB)
servo=PWM(Pin(15),freq=50)
while True :
x=(adc.read()/22.75)
iLED4.writeDigitNum(0,x//1000,0)
iLED4.writeDigitNum(1,x%1000//100,0)
iLED4.writeDigitNum(2,x%100//10,0)
iLED4.writeDigitNum(3,x%10,0)
iLED4.writeDisplay()
sleep(0.1)
servo.duty(int(x))

## Slide 9: เมื่อ sonar มีค่า = 0 ให้ไฟ ZX RGB3R ติด
from machine import Pin,ADC
from time import sleep
from neopixel import NeoPixel
import display
np = NeoPixel(Pin(15, Pin.OUT), 3)
adc = ADC(Pin(32))
adc.atten(ADC.ATTN_11DB)
while True :
print('ADC=',adc.read(),'Rang',adc.read()/40.95)
sleep(0.5)
if adc.read() == 0:
np.fill((30,0,0))
np.write()
else :
np.fill((0,0,0))
np.write()

## Slide 10: POT เปลี่ยน หลอด LED
import math
from machine import Pin,ADC
from time import sleep
import display
adc = ADC(Pin(32))
adc.atten(ADC.ATTN_11DB)
led1=Pin(4,Pin.OUT)
led2=Pin(15,Pin.OUT)
led3=Pin(2,Pin.OUT)
while True :
print(adc.read())
if adc.read() <= 1365 :
led1(1)
led2(0)
led3(0)
elif adc.read() <= 2047 :
led1(0)
led2(1)
led3(0)
elif adc.read() >= 2047 :
led1(0)
led2(0)
led3(1)

## Slide 11: POT เปลี่ยน หลอด LED โชว์เลขที่จอ OLED
import math
from machine import Pin, ADC
from time import sleep
import display
import OLED
adc = ADC(Pin(32))
adc.atten(ADC.ATTN_11DB)
oled = OLED.SSD1306_I2C(128, 64)
led1 = Pin(4, Pin.OUT)
led2 = Pin(15, Pin.OUT)
led3 = Pin(2, Pin.OUT)
while True:
sensor_value = adc.read()
print(sensor_value)
oled.text(str(sensor_value), 0, 0, 1)
oled.show()
sleep(0.5)
if sensor_value <= 1365:
led1.on()
led2.off()
led3.off()
elif 1365 < sensor_value <= 2047:
led1.off()
led2.on()
led3.off()
elif sensor_value > 2047:
led1.off()
led2.off()
led3.on()

## Slide 12: รับ
import ESPNOW as now
import display
while True:
if now.isReadyToRead():
print((now.getSenderMAC()))
print((now.readAsText()))
display.show('R', display.hex2byte('#ff0000'))
now.send('รับ', (now.getSenderMAC()))

## Slide 13
import OLED
from machine import Pin,ADC,PWM
from time import sleep
adc = ADC(Pin(32)) # P2
adc.atten(ADC.ATTN_11DB)
servo=PWM(Pin(15),freq=50)
oled = OLED.SSD1306_I2C(128, 64)
while True :
x=(adc.read()/22.75)
oled.text(str(x),0,0,1); oled.show()
sleep(0.1)
servo.duty(str(x))